## Slide 1: Zone-wise PQC and QKD for SMR control systems
M.Sc. THESIS PROPOSAL · REVISED APPROACH
Where does post-quantum cryptography suffice, and where does QKD add measurable value?

## Slide 2: Why the approach changed
Wrong threat model
Nuclear I&C ranks availability and integrity above confidentiality. The urgent quantum risk is firmware roots of trust and long-retention data.
Attacks crypto cannot stop
Process-level attacks and Stuxnet-type malware bypass link encryption, so they cannot judge a cryptographic choice.
Weak comparison
RSA/AES baseline, QKD-only without authentication, and an index with arbitrary weights.

## Slide 3: High-level architecture

## Slide 4: The five zones
Zone | Typical assets | Trust and data flow | Crypto role
Z1 Safety | Reactor protection, safety I&C | Most trusted; one-way outbound | Signed firmware; pre-shared keys
Z2 Control | DCS, PLCs, field switches | Controlled flow from Z1 | MACsec at boundaries
Z3 Supervisory | SCADA, HMI, historian | Operators and engineers | Hybrid key exchange; signed commands
Z4 DMZ / remote | Jump hosts, vendor access | Brokered, untrusted callers | Hybrid KEM; ML-DSA PKI
Z5 Enterprise | Business IT, regulator links | Least trusted | Hybrid TLS; optional QKD link

## Slide 5: Threat surfaces of a nuclear ICS
Remote access
Vendor support, remote monitoring and operations links crossing the DMZ.
IT/OT boundary
Historians, enterprise networks and data gateways between zones.
Engineering endpoints
Maintenance laptops, USB media and engineering workstations that reach controllers.
Supply chain and firmware
Digital I&C, FPGA logic and updates with 40–60-year lifetimes.
Field and network layer
Switches, fibre taps, wireless links and unauthenticated protocols such as Modbus.
Data and insiders
Design, safeguards and physical-protection data; privileged staff and physical access.

## Slide 6: What PQC and QKD can and cannot reach
PQC helps with
Identity and mutual authentication (ML-DSA), signed firmware (SLH-DSA/LMS), key exchange (ML-KEM) that stays safe against quantum attack.
QKD helps with
Fresh symmetric keys on fixed fibre links, and long-term confidentiality for selected flows. It still needs authentication.
Not solved by crypto
Compromised endpoints, USB and insider misuse, process-logic attacks, firmware compromised before signing, and denial of service.

## Slide 7: STRIDE analysis (1 of 2)
Threat | Nuclear ICS example | PQC | QKD | Still needed
Spoofing | Rogue device or vendor impersonation | ML-DSA mutual authentication, quantum-safe identity | No direct help; needs authenticated channel | Device allowlisting, MFA
Tampering | Setpoint injection, replay, forged firmware | Signed firmware (SLH-DSA/LMS), authenticated encryption | Fresh keys for message authentication | Data diodes, process-level checks
Repudiation | Disputed commands or maintenance actions | ML-DSA signatures on commands and logs | None: symmetric keys cannot prove origin | Audit logging, time sync
Notes: S, T, R. QKD gives no non-repudiation.

## Slide 8: STRIDE analysis (2 of 2)
Threat | Nuclear ICS example | PQC | QKD | Still needed
Information disclosure | Eavesdropping; harvest-now-decrypt-later of design and safeguards data | Hybrid ML-KEM key exchange | Seeds keys for long-confidentiality fixed links | Data classification, retention limits
Denial of service | Flooding; key-supply loss; fibre cut or alarm | Adds handshake load; larger packets | Alarm or fibre cut stops key supply | PQC fallback, redundancy, rate limits
Elevation of privilege | Rogue engineering workstation or stolen credentials | Role-bound certificates, signed commands | None | Least privilege, segmentation
Notes: I, D, E. Crypto can create new availability risks.

## Slide 9: Dominant threats and response by zone
Zone | Dominant STRIDE threats | Cryptographic response
Z1 Safety | Tampering, denial of service | No remote keys; data diode; signed firmware
Z2 Control | Spoofing, tampering, DoS | MACsec at boundaries; PQC fallback
Z3 Supervisory | Spoofing, tampering, repudiation, elevation | ML-DSA authentication; signed commands and logs
Z4 DMZ / remote | Spoofing, disclosure, elevation, DoS | Hybrid KEM; ML-DSA PKI
Z5 Enterprise | Disclosure, spoofing, repudiation | Hybrid TLS; QKD-seeded links where fibre is fixed

## Slide 10: One question, five setups
For each IEC 62443 zone, which profile meets the target security level within the control-loop delay margin, key-supply limits and regulatory constraints?
1 | 2 | 3 | 4 | 5
Plaintext legacy | Classical ECDHE + AES-256 | PQC-only | Classical + PQC | PQC + QKD-seeded keys

## Slide 11: Key management by zone
Zone | Cryptographic profile
Z1 Safety | One-way data diode, no remote keys, pre-shared AES-256, PQC-signed firmware. No QKD.
Z2 Control | MACsec AES-256 at boundaries, PLCs unmodified; QKD-seeded keys with PQC fallback
Z3 Supervisory | IKEv2 with ML-KEM plus QKD-seeded key; OPC UA via gateway
Z4 DMZ / remote | Hybrid X25519 + ML-KEM-768, ML-DSA certificates
Z5 Enterprise | Hybrid TLS 1.3; QKD only on fixed dark-fibre sites

## Slide 12: Making QKD defensible
Authenticate it
Pre-shared Wegman–Carter key or ML-DSA, stated explicitly.
Finite-key bounds
Composable bound with explicit secrecy and correctness errors; decoy states bound PNS.
Combine safely
KMAC256 with zone, conduit and transcript context.
Fail gracefully
QKD outage switches to PQC-only keys; never fail closed.

## Slide 13: How it will be evaluated
Emulated testbed
OpenPLC + Mininet + reactor model. Measure handshake and rekey delay and control-loop delay margin.
Zone index (ZPI)
Break-both rule for QKD + PQC; weakest-link-aware aggregation; AHP weights favouring availability and integrity.
Validation
Effect sizes with CIs, Morris/Sobol sensitivity, Kendall rank correlation with security levels, expert review.

## Slide 14: Outputs and next steps
Zone-wise recommendation: where PQC suffices, where QKD adds value
Phased PQC migration path: inventory, hybrid at boundaries, device roots of trust
Next: confirm co-supervisor, source the testbed topology, budget the hardware